## Slide 1: Remote Landslide Observation System with Differential GPS
2012 International Conference on Structural Computation and Geotechnical Mechanics
Author: Xing ZHU, Qiang XU, Jianbin ZHOU, Maolin DENG.
Date:2013/08/21
Speaker : Da-Wei Yang

## Slide 2: Outline
Introduction
Remote Observation System
Hardware and Software
Experimental tests
Field Application
Test results
Conclusion

## Slide 3: Introduction
With aim to master early deformation stages and motion laws of landslide, the raw displacement data of landslide are very important for the landslide researchers and environmental scientists.

## Slide 4: Introduction
The paper developed a landslide displacement remote observation system based on differential GPS technology to get the raw displacement data continually.

## Slide 5: Hardware
A GPS-based observation system includes at least two GPS observation stations, one of which is the reference point and the other is the measuring point.

## Slide 6: Software
Remote Control Center has the task of collecting data from all GPS receivers in the network and post-processing the GPS data from the reference point and the measuring point.

## Slide 7: Remote Observation System

## Slide 8: Remote Observation System
The GPS-based displacement observation system is capable of three-dimensional, real-time, and high accuracy (mm level).
北
東
高

## Slide 9: Experimental tests
The measuring base-line distance between two GPS stations is 3.7km.
The results show us that this system has a high observation precision with sub-centimeter of about ±8mm.
Generally speaking, because the dynamics associated with geotechnical movements are very slow (mm/year to cm/day) and similar to static measuring, this system can meet the need of landslide movement observation.

## Slide 10: Experimental tests

## Slide 11: Field Application

## Slide 12: Field Application
On the landslide area there is a GPS measuring station at 1662m. The base-line distance between the reference station and the monitoring station was 767.7315m when the observation stations were installed.

## Slide 13: Test results
19th April to 20th July.
The base-line distance from the reference station to the measuring station is 767.7315m on 19th April and 876.9213m on 20th July according to software calculation.
A large-scale destruction on 15th July induced by a rainstorm, so this observation is very important for this landslide research.

## Slide 14: Test results

## Slide 15: Test results

## Slide 16: Conclusion
The system measuring in static mode every 15 minutes, the measurement accuracy is about ±8mm and meets the needs of landslide displacement observation.
The GPS-based system can be used to remote monitor the large-scale deformation of landslides in near-real time. At the same time, we can get the landslide deformation stage from the change trend of displacement curves.

## Slide 17: Conclusion
The GPS-based system can record the displacement history at any moment and this is very important to the geohazard prevention and study.