## Slide 1: UPnP Device Architecture
Presenter: Chelsea

## Slide 2: Outline
What is UPnP?
What components does UPnP offer?
What protocol does UPnP use?
How does UPnP work?
Summary

## Slide 3: UPnP (Universal Plug and Play)
Derived from the PnP(Plug and Play)
What services does UPnP offer?
  Zero-Configuration
  Auto Discovery

## Slide 4: What components does UPnP offer?
Device
Control Point
Service
UPnP Enable Device
Device
Service 1
Service 2
Control Point
UPnP Enable Device
Control Point
Device
Service
UPnP Enable Device
Root Device
Service
Service 1
Service 2
Embedded Device
Notes: CCID 4 experiment use 1500 bytes
Acknowledgement mechanisms communicating packet loss and ECN information.

## Slide 5: What protocol does UPnP use?
GENA(Generic Event Notification Architecture)
  GENA is based on HTTP
  GENA defines an HTTP notification architecture that transmits notifications between HTTP resources.
SOAP(Simple Object Access Protocol)
  SOAP uses XML Information Set for its message format
Notes: The cookie mechanism aims to avoid Denial-of-Service attacks, which were found to exploit the vulnerability of three-way handshakes of TCP.
During the association establishment, the client and the server of SCTP can negotiate the number of stream in an association.
可以選擇開啟多少個stream

## Slide 6
SSDP(Simple Service Discovery Protocol)
  Feature :
    Control point can search the special services what it need of device in the same subnet by SSDP.
    Device can announce about its message to the control point who is in the same subnet by SSDP.
  Architecture:
    SSDP is based on HTTPU ( HTTP with UDP )
    Port number is 1900
    In IPv4, the multicast address is 239.255.255.250
    In IPv6, the multicast address is FF0X::C
  Method :
    M-SEARCH :「ssdp:discovery」
    M-NOTIFY : 「ssdp:alive」 & 「ssdp:byebye」

## Slide 7: UPnP protocol stack

## Slide 8: How does UPnP work?
Addressing
Discovery
Description
Eventing
Control
Presentation
Addressing
Discovery
Description
Control
Presentation
Eventing
Notes: mapping from the subflow sequence number to the data sequence number

## Slide 9
Addressing
  DHCP (Dynamic Host Configuration Protocol)
  Auto-IP (Automatic IP addressing)

## Slide 10
Discovery
  SSDP

## Slide 11
Description

## Slide 12
Control
  SOAP

## Slide 13
Eventing
  GENA
  Unicast eventing architecture

## Slide 14
Presentation

## Slide 16: Summary
UPnP technology brings convenience to our life.
It is not very widely used now.
UPnP is intended primarily for residential networks.

## Slide 17: Questions and Comment

## Slide 18: Reference
http://upnp.org/specs/arch/UPnP-arch-DeviceArchitecture-v1.1.pdf
https://en.wikipedia.org/wiki/Universal_Plug_and_Play
http://jita.csi.chu.edu.tw/Jita_web/publish/vol5_num4/5.pdf
http://speed.cis.nctu.edu.tw/~ydlin/miscpub/survey_UPnP.pdf