## Slide 1: NDN (Named Data Networking)
Presenter: Chelsea

## Slide 2: Outline
What is NDN?
Why we need NDN?
NDN architecture and packet format
How does NDN work?
Summary
Reference

## Slide 3: NDN (Named Data Networking)
It is one of five projects funded by the U.S. National Science Foundation under its Future Internet Architecture Program.
It has its roots in an earlier project, Content-Centric Networking(CCN).
  CCN was first publicly presented in 2006 by Van Jacobson.
  The evolution from today’s host-centric network architecture to a data-centric network architecture.
host-centric network architecture
IP(Internet protocol)
data-centric network architecture
NDN

## Slide 4: Why we need NDN?
Nowadays networking is based on TCP/IP
  Advantage :
    TCP/IP packets named only communication endpoints.
  Disadvantage :
    Security
    Flexibility
    Broadcast

## Slide 5: NDN Architecture
IP architecture
NDN architecture
Notes: The main building blocks of NDN architecture are named content chunks, in contrast to the IP architecture’s fundament unit of communication, which is and end-to-end channel between two endpoints identifiered by IP address

## Slide 6: NDN packet format
Notes: Packets in NDN architecture

## Slide 7: Content Naming
Names are generated by application
Hierarchical – identify content relationship and facilitate aggregation
Every data packets carried a signature, binding name to the content
NCNU-CSIE/videos/badminton/1(version)/2(segment)
Routed name
application
Application instance

## Slide 8: What components are in NDN router?
To carry out the Interest and Data packet forwarding function, each NDN router maintains three data structures and a module :
  PIT ( Pending Information Table)
  FIB (Forwarding Information Base)
  CS (Content Store)
  Forwarding Strategy module

## Slide 9: Forwarding process at an NDN node
CS
PIT
FIB
Request A
Interest
Data producer
forward
Data
Add incoming interface
Notes: Forwarding process at an NDN node

## Slide 10: Forwarding process at an NDN node
CS
PIT
Request A
Data producer
forward
Data
Remove entry
Notes: Forwarding process at an NDN node

## Slide 11: Forwarding process in NDN
Request A
Data producer
NDN Router
Request B
Interest packet
Data packet
CS
PIT

## Slide 12: Forwarding process in NDN
Request A
Data producer
NDN Router
Request B
Interest packet
Data packet
CS

## Slide 13: Forwarding process in NDN
Request A
Data producer
NDN Router
Request B
Interest packet
Data packet

## Slide 14: Nowadays Networking
Data producer

## Slide 15: Named Data Networking
Data producer

## Slide 16: Summary
 | NDN | TCP/IP
completely transmission | 2 packets (Not connection based) | 9 packets (Connection based)
Security | Great | Bad
Routing and forwarding problem | Matching integers is much faster | Insufficient IP address NAT traversal Mobility Wasting of resource
NCE
(Name Component Encoding)

## Slide 17: Questions and Comment

## Slide 18: Reference
Named Data Networking architecture
  L. Zhang, A. Afanawyev, J. Burke, V. Jacobson, K. Claffy, P. Crowley et al., “Named Data Networking,” ACM SIGCOMM Computer Communication Review, Vol. 44, No. 3, July 2014.
Named Data Networking Test-bed
Quickly understand NDN by video
Introduction NDN by Van Jacobson