## Slide 1: ACT:Audio Conference Tool Over Named Data Networking(NDN)
Authors: Zhenkai Zhu UCLA, Los Angeles, CA, USA
Sen Wang Tsinghua University, Beijing, China
Xu Yang Tsinghua University, Beijing, China
Van Jacobson PARC, Palo Alto, CA, USA
Lixia Zhang UCLA, Los Angeles, CA, USA
Published in: ICN ‘11 Proceeding of the ACM SIGCOMM workshop on Information-centric networking Page 68-73

## Slide 2: Outline
How does NDN work
ACT design
  Conference Discovery
  Speaker Discovery
  Voice Data Distribution
Summary

## Slide 3: Named Data Networking
Interest
Router
FIB (Forwarding Interface Base)
PIT (Pending Interest Table)
Content Store
Notes: Interest - The packet that request for desired data.
Router - Remember which interface the request comes in, looks up the name in Forwarding Interface Base(FIB) and removes the PIT entry and caches the Data in the Content Store.
FIB - Populate by routing protocol that propagate name prefixes instead of IP prefixes.
PIT (Pending Interest Table) - To store the same Interest. When the Data packet arrives, the router sends a copy to each of the interfaces in the corresponding PIT entry.
Content Store – The router’s basic buffer memory.

## Slide 4
Request
Router
Server
FIB
2.Look up the name in FIB
1.Send Interest
3.Forward Interest
4.Return Data
5.Return Data

## Slide 5
Request A
Request B
Request C
Router
(Content Store)
Server
1.Send Interest
2.Send Interest
3.Send Interest
4.Only forwarding the first Interest
FIB
5.Look up the name in FIB
6.Forward Interest
7.Retrun Data
PIT
8.Send a copy to each of the interfaces in the corresponding PIT entry
9.Return Data
10.Return copied Data
11.Return copied Data
12.Remove the PIT entry and cache in the Content Store

## Slide 6: ACT Design
Conference Discovery:
Collect the latest information about all existing conferences.
Speaker Discovery:
Find the speakers in a conference.
Voice Data Distribution:
The information about the Voice data

## Slide 7: Namespace
Broadcast namespace
  For conference discovery, speakers discovery
User location based namespace
  For voice data delivery

## Slide 8: Conference Discovery
The name for conference data within NDN
( /ndn/broadcast/conference/conference-list)
/ndn The scope of network
/broadcast Broadcast name space
/conference Application type
/conference-list The data that the participant is interested in

## Slide 9: Conference Announcement
SDP (Session Description Protocol)
  Estimated starting time
  Media type supported
  Etc.
Appending conference name to the prefix “conference-list”

## Slide 11: Conference Enumeration
Discovery module
Interest
Broadcast
conference-list
A : icn2011
Discovery module
Interest
Broadcast
conference-list
Any other node
Ex: (D: icn20XX)
(Exclusion Filter)
A: icn2011

## Slide 12: Conference List Maintenance
Discovery module
Known conference
refresh time
remove time
When T(refresh) time out
Discovery module
Interest
Broadcast
conference-list
(New) A : icn2011
(Exclusion Filter)
A: icn2011
T(remove) = T(refresh) + maximum delay to retrieve data
When T(remove) time out, the conference should be removed from the conference list

## Slide 13: Speaker Discovery
The mechanism of speaker discovery is similar to conferences discovery
(/ndn/broadcast/conference/[conference-name]/speak-list)
ACT scale well
only track a list of active speakers

## Slide 14: Voice Data Distribution
Each speaker uses topology-dependent name prefix for its voice data
(/ucla.edu/cs/zhenkai/[device-id]/[codec-name]/[seg-num])
device-id 32-bit random string
seg-num sequentially named and stored in a circular buffer

## Slide 15: Summary
The intermediate routers can reduce most repeated packets.
If server crash or disconnect, the traditional method couldn’t continue the conference but NDN could.

## Slide 16: Reference
Zhenkai Zhu et al., ACT: Audio Conference Tool Over Named Data Networking , Proceedings of the ACM SIGCOMM workshop on Information-centric networking (ICN'11), pp. 68-73, August 19, 2011.
Session Description Protocol