## Slide 1: SIP Forking
107214005 田蕙瑜 2020/12/01

## Slide 2: SIP Message — Request or Response
Request:
  REGISTER, INVITE, ACK, BYE, CANCEL, MESSAGE etc.
Response(Status code):
1xx: Provisional; 2xx: Success; 3xx: Redirection
4xx: Client Error; 5xx: Server Error; 6xx: Global Failure
Source
Destination
Info.
[註] Client IP: 10.21.22.197; SIP Server IP: 163.22.20.111
Notes: The interpretation of the body depends on the request method.
All responses MAY include a body.
舉例來說，通常Request INVITE會有body to give interpretation of devices
---
1xx: Provisional
-- request received, continuing to process the request;
2xx: Success
-- the action was successfully received, understood, and accepted;
3xx: Redirection
-- further action needs to be taken in order to complete the request;
4xx: Client Error
-- the request contains bad syntax or cannot be fulfilled at this server;
5xx: Server Error
-- the server failed to fulfill an apparently valid request;
6xx: Global Failure
-- the request cannot be fulfilled at any server.

## Slide 3: Transaction
Def. a SIP transaction consists of a single request and any responses to that request
Type:
  INVITE Transaction: It consists of a three-way handshake.
  Non-INVITE Transaction: It do not make use of ACK.
Notes: The INVITE transaction consists of a three-way handshake.
The client transaction sends an INVITE, the server transaction sends responses, and the client transaction sends an ACK.
Non-INVITE transactions do not make use of ACK.

## Slide 4: CSeq(Command Sequence)
Def.
  The CSeq header field serves as a way to identify and order transactions.
  It consists of a sequence number and a method.

## Slide 5
Request-Line: MESSAGE sip:chris@163.22.20.111 SIP/2.0
Message Header:
  Via: SIP/2.0/UDP 10.72.21.52:5060;branch=z9hG4bK.AgnKm6ux8;rport
  From: <sip:alice@163.22.20.111>;tag=fP3~vWwX~
  To: sip:bob@163.22.20.111
  CSeq: 20 MESSAGE
  Content-Type: text/plain
  Content-Length: 2
  User-Agent: Linphone Desktop/4.2.2 (Windows 10 Version 2004, Qt 5.14.2) LinphoneCore/4.4.0-13-gc99cb9c88
Message Body:
  Line-based text data: text/plain (1 lines)
    hi
SIP Message — Request

## Slide 6
Status-Line: SIP/2.0 200 Ok
Message Header:
  Via: SIP/2.0/UDP 10.72.21.52:5060;received=10.72.21.52;branch=z9hG4bK.AgnKm6ux8;rport=5060
  From: <sip:alice@163.22.20.111>;tag=fP3~vWwX~
  To: <sip:bob@163.22.20.111>;tag=A8slvPo
  Call-ID: ZEkBue-znE
  CSeq: 20 MESSAGE
    Sequence Number: 20
    Method: MESSAGE
SIP Message — Response

## Slide 7: A SIP Call: Chris called Bob, Bob answered and hung up
INVITE
100Trying
INVITE
180 Ringing
180 Ringing
200 OK
200 OK
ACK
SIP Server
163.22.20.111
Chris
10.21.22.197
Bob
10.21.24.21
ACK
BYE
BYE
200 OK
200 OK
Notes: # After BYE,
# 例如: IVITE我們正在I180Ring我們正在處裡訂單：200OK訂單有貨

## Slide 8: DEMO1 – A SIP Call
Wireshark setting:
  Capture filter: udp port 5060
  Display filter: sip
  Listen on the Ethernet
Scenario (Wireshark run on Chris):
  Chris IP: 10.21.22.197
  SIP Server IP: 163.22.20.111

## Slide 9: SIP Forking
INVITE
100Trying
INVITE
180 Ringing
180 Ringing
200 OK
200 OK
ACK
SIP Server
163.22.20.111
Bob(Win10)
10.21.22.197
Alice
10.21.24.17
ACK
200 OK
Bob(Mac)
10.21.24.21
INVITE
180 Ringing
ACK
180 Ringing
487
Request
terminated
CANCEL
Alice call Bob,
but there are 2 Bobs…
=> INVITE will be forked.

## Slide 10: SIP Forking
INVITE
100Trying
INVITE
180 Ringing
180 Ringing
200 OK
200 OK
ACK
SIP Server
163.22.20.111
Bob(Win10)
10.21.22.197
Alice
10.21.24.17
ACK
200 OK
Bob(Mac)
10.21.24.21
INVITE
180 Ringing
ACK
180 Ringing
487
Request
terminated
CANCEL
CANCEL sip:bob@10.21.22.197; transport=udp SIP/2.0
Via: SIP/2.0/UDP 163.22.20.111;branch=z9hG4bKfb7a.65535e1962a113109ef75150be3a9b4c.1
From: <sip:alice@163.22.20.111>; tag=-lJp4Ghc~
To: sip:bob@163.22.20.111
CSeq: 20 CANCEL
Call-ID: wz~TVHXav5
Max-Forwards: 69
Content-Length: 0
Reason: SIP;cause=200; text="Call completed elsewhere"

## Slide 11: DEMO2 – SIP Forking
Wireshark setting:
  Capture filter: udp port 5060
  Display filter: sip
  Listen on the Ethernet
Scenario (Wireshark run on Bob’s PC):
  Alice call 2 Bob
  Bob call 2 Alice