## Slide 1: Brief Introduction of RDMA (Remote Direct Memory Access)
資工二 田蕙瑜

## Slide 2: OUTLINE
WHAT IS RDMA?
WHY WE NEED RDMA? 3 Advantages
REALIZATION OF RDMA

## Slide 3: WHAT IS RDMA?
DMA (Direct Memory Access)
  它允許某些電腦內部的硬體子系統（電腦外設），可以獨立地直接讀寫系統記憶體，而不需中央處理器（CPU）介入處理 。
  DMA傳輸常使用在將一個記憶體區從一個裝置複製到另外一個，例如移動一個外部記憶體的區塊到晶片內部更快的記憶體去。

## Slide 4: WHAT IS RDMA?
RDMA (Remote DMA)
  Low latency and high throughput
  RDMA技術最早出現在Infiniband網路
  傳統的基於Socket (TCP/IP Protocol)的網路通訊，資料在系統DRAM、處理器Cache和網絡卡Buffer之間來回拷貝搬移，因此佔用了大量的CPU計算資源和記憶體匯流排頻寬，也加大了網路延時。
Notes: 舉例來說，40Gbps的TCP/IP流能耗盡主流伺服器的所有CPU資源；RDMA則解決了傳統TCP/IP通訊的技術痛點。例如，在40Gbps場景下，CPU佔用率從100%下降到5%，網路延時從ms級降低到10us以下。

## Slide 5: RDMA Protocol for Better Efficiency
Zero Copy
Kernel bypass
No CPU involvement

## Slide 6: ZERO COPY

## Slide 7: ZERO COPY

## Slide 8: ZERO COPY

## Slide 9: Bypassing the Operating system
Kernel bypass

## Slide 10: Bypassing the Operating system
Zero Copy

## Slide 11: How RDMA works?
a Network Interface Card(NIC)
Host Channel Adapter(HCA)

## Slide 13: How RDMA works?

## Slide 14: REALIZATION OF RDMA
Infiniband:
  a networking protocol that supports RDMA. It needs hardware support.
RoCE(RDMA over Converged Ethernet)
  a networking protocol that allows RDMA over Ethernet network.
iWARP

## Slide 16: WHY WE NEED RDMA?
HPC 處重於高效能的演算，並透過軟體平行連結的機制串聯大量高速主機(電腦叢集 computer cluster)。可以想像成藉由網路將多個電腦串連成一台超級電腦。
因此，需要RDMA的高速傳送及讀取資料，且不能影響到CPU的效能。

## Slide 17: Reference
Understanding the concepts and mechanisms of RDMA
關於RDMA技術原理、三種主流實現技術對比
RDMA Aware Networks Programming User Manual
RDMA Introduction